## Slide 1
Lecture 4 Fourier Series of Continuous-time Signals
School of Computer Engineering and Science
Shanghai University
Instructor: Jianjia Wang, Shengyu Duan

## Slide 2: Outline: Lecture 4: Fourier Series of Continuous-time Signals 连续时间信号的傅立叶级数
Time/Frequency Domain（时域频域）
Response of LTI Systems to Exponential SignalLTI 系统对指数信号的反应
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 3: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 4: Time/Frequency Domain
Time domain signal（时域）
A signal is a function, in the mathematical sense, normally a function of time.在数学意义上，信号是一种函数，通常是时间的函数。

## Slide 5: Time/Frequency Domain
Time domain signal
Time domain analysis examines the amplitude vs. time characteristics of a measuring signal.时间域分析检查测量信号的振幅与时间特征。
Time domain is how people tend to think that things work, but in many situations, signals in time domain can be complicated.

## Slide 6: Time/Frequency Domain
Time domain signal
We can easily observe the loudness of a sound, but what else?
  - Whose voice is this?
  - How much is the noise?
An audio signal in time domain

## Slide 7: Time/Frequency Domain
Frequency domain（频域）
In 1807, J.B.J Fourier proposed to use trigonometric functions and series to solve heat equation in a metal plate.
Fourier claimed any arbitrary periodic function can be represented by a harmonically related trigonometric series.
Fourier series representation:傅里叶级数表示:

## Slide 8: Time/Frequency Domain

## Slide 9: Time/Frequency Domain
Frequency domain
Frequency domain shows how much of the signal lies within each given frequency band over a range of frequencies.
（频率域显示每个给定频率带内的信号在一系列频率中的多少）
）
Time domain signal
Frequency domain signal

## Slide 10: Time/Frequency Domain
Why frequency domain is important
We can collect even more information in frequency domain, e.g.:
  - Speaker recognition based on frequency-based coefficients
  - Noise identification based on noise frequency characteristics
An audio signal in frequency domain

## Slide 11: Time/Frequency Domain
Why frequency domain is important
Frequency domain is a different perspective on signal, which providing us more useful information.
Generally,
- Time domain shows how we tend to think that things work;
时间域显示我们如何倾向于认为事情是工作;
  - Frequency domain can often provide many detailed performance specifications.频率域通常可以提供许多详细的性能规范。

## Slide 12: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 13: Response of LTI Systems to Exponential Signal LTI系统对指数信号的响应
Fourier series sine-cosine form
Sinusoids can be represented by complex exponential function
（正弦信号可以用复指数函数表示）

## Slide 14: Response of LTI Systems to Exponential Signal
Fourier series exponential form 傅里叶级数指数形式

## Slide 15: Response of LTI Systems to Exponential Signal
Fourier series exponential form
Assume

## Slide 16: Response of LTI Systems to Exponential Signal
Fourier series exponential form

## Slide 17: Response of LTI Systems to Exponential Signal
Assume
LTI

## Slide 18: Response of LTI Systems to Exponential Signal
LTI

## Slide 19: Response of LTI Systems to Exponential Signal LTI 系统对指数信号的反应
is a constant（常数）, thus we define :
LTI

## Slide 20: Response of LTI Systems to Exponential Signal
Response of a LTI system to an exponential signal is this exponential signal multiplied with a constant.
(LTI系统对指数信号的响应是这个指数信号乘以一个常数)
We call an exponential function, , as the eigenfunction of any LTI system.(我们称指数函数为任何 LTI 系统的电子函数)
We call the constant, , as the eigenvalue associated with the eigenfunction .

## Slide 21: Response of LTI Systems to Exponential Signal
Why do we specifically study LTI response to exponential signal?
Fourier series can be considered as a composition of exponential signals:
傅立中系列可视为指数信号的组成：

## Slide 22: Response of LTI Systems to Exponential Signal
Why do we specifically study LTI response to exponential signal?
LTI response to a periodic signal represented by Fourier series is still a periodic signal represented by Fourier series.(LTI 对以傅立元系列为代表的周期性信号的响应仍然是以傅立元系列为代表的周期性信号。
)
LTI

## Slide 23: Response of LTI Systems to Exponential Signal
If the input has a frequency component, the output will exactly have the same frequency component, except scaled by a constant.
如果输入复指数函数，输出将完全具有相同的复指数函数，但按常数缩放除外。
Frequency domain（频域）:

## Slide 24: Response of LTI Systems to Exponential Signal
Each frequency component never split to other frequency components, no convolution involved, realizing fast and convenient signal processing.
每个频率分量不分裂到其他频率分量，不涉及卷积，实现了快速方便的信号处理。

## Slide 25: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 26: Fourier Series Representation
Harmonically related complex exponentials
A harmonic of such a wave is a wave with a frequency that is a positive integer multiple of the frequency of the original wave, known as the fundamental frequency. 这种波的谐波是具有正整数倍于原始波频率（称为基本频率）的波。
Fundamental frequency: ()
2nd harmonic: 2 ()
3rd harmonic: 3 () …

## Slide 27: Fourier Series Representation
Fourier series sine-cosine form
Fourier series amplitude-phase form

## Slide 28: Fourier Series Representation
Amplitude-phase form derived from exponential form振幅-相位形式由指数形式衍生而来

## Slide 29: Fourier Series Representation
Amplitude-phase form derived from exponential form振幅-相位形式由指数形式衍生而来
Remember in slide 16, we have assumed: , thus and (for ) are a pair of complex conjugates.
and (for ) are a pair of complex conjugates.
and (for ) are also a pair of complex conjugates
也是一对复杂的结合体
.

## Slide 30: Fourier Series Representation
Amplitude-phase form derived from exponential form
Remember in slide 16, we have assumed: , thus and (for ) are a pair of complex conjugates.
Note that the above hypothesis is true, only if and are real, and thus the signal is a real signal.请注意，上述假设是正确的，只有当Ak和Bk是真实的，信号是一个真正的信号。

## Slide 31: Fourier Series Representation
Amplitude-phase form derived from exponential form
Remember in slide 16, we have assumed: , thus and (for ) are a pair of complex conjugates.
and (for ) are a pair of complex conjugates.
and (for ) are also a pair of complex conjugates.

## Slide 32: Fourier Series Representation
Amplitude-phase form derived from exponential form

## Slide 33: Fourier Series Representation
Amplitude-phase form derived from exponential form
Use polar coordinate system to represent as:

## Slide 34: Fourier Series Representation
Determination of Fourier series coefficient - 傅里叶级数系数的确定

## Slide 35: Fourier Series Representation
Determination of Fourier series coefficient -

## Slide 36: Fourier Series Representation
Determination of Fourier series coefficient -
For k=n:
For kn:

## Slide 37: Fourier Series Representation
Determination of Fourier series coefficient -

## Slide 38: Fourier Series Representation
Fourier series representation:
Fourier series coefficient:傅里叶级数系数:

## Slide 39: Fourier Series Representation
Example:
Find Fourier series coefficients for the following periodic signal.
查找以下周期信号的傅立物级数系数。

## Slide 40: Fourier Series Representation
Solutions:

## Slide 41: Fourier Series Representation
Assume
Spectral:

## Slide 42: Fourier Series Representation
Assume
But is this correct?

## Slide 43: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 44: Convergence Issue
Question:
In time domain, this signal is not continuous with discontinuity.在时域中，该信号不是不连续的连续信号。
In frequency domain, this signal is represented by a trigonometric series, each of which is continuous.在频域，这个信号用一个三角级数表示，每个三角级数都是连续的。
How is the discontinuity represented?

## Slide 45: Convergence Issue
Gibbs phenomenon

## Slide 46: Convergence Issue
Gibbs phenomenon
The partial sum of the Fourier series has large oscillations near the jump, which might cause a fixed overshoot above the function itself.
傅里叶级数的部分和在跳跃附近有很大的振荡，这可能导致函数本身的固定超调。
As the number of terms rises, the error of the approximation is reduced in width and energy.
随着项数的增加，近似的误差在宽度和能量上减小。
At the jump discontinuities, the limit will converge to the average of the values of the function on either side of the jump. (Dirichlet Theorem)
在跳跃不连续点处，极限将收敛于跳跃两侧的函数值的平均值。(狄利克雷定理)

## Slide 47: Convergence Issue
A period signal can be represented by Fourier series, if it has finite energy:
周期信号可以用傅立叶级数表示，如果它的能量有限:

## Slide 48: Convergence Issue
Dirichlet’s condition
A signal can be represented by Fourier series expansion, if
一个信号可以用傅立叶级数展开表示，如果
(1) it is absolutely integrable,
它绝对是可积的
(2) it has finite number of maxima & minima in a period
它在一个周期内有有限数量的最大值和最小值
(3) it has finite number of discontinuities in a period
它在一个周期内有有限数量的不连续点

## Slide 49: Convergence Issue（收敛问题）
Dirichlet’s condition（狄利克雷条件）
A signal can be represented by Fourier series expansion, if
一个信号可以用傅立叶级数展开表示，如果
(1) it is absolutely integrable（它绝对是可积的）,
The signal below can not be represented by Fourier series expansion:
下面的信号不能用傅里叶级数展开表示:

## Slide 50: Convergence Issue收敛性问题
Dirichlet’s condition
A signal can be represented by Fourier series expansion, if
(2) it has finite number of maxima & minima in a period
它在一个周期内有有限数量的最大值和最小值
The signal below can not be represented by Fourier series expansion:

## Slide 51: Convergence Issue
Dirichlet’s condition
A signal can be represented by Fourier series expansion, if
(3) it has finite number of discontinuities in a period
它在一个周期内有有限数量的不连续点
The signal below can not be represented by Fourier series expansion:

## Slide 52: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 53: Fourier Series Properties傅里叶级数的性质
The following notation is used to indicate a signal, , can be represented by Fourier series with the coefficients, .
下面的符号用来表示一个信号𝑥(𝑡)，可以用傅里叶级数的系数表示

## Slide 54: Fourier Series Properties
Linearity 线性
Assume :
,
Then:

## Slide 55: Fourier Series Properties
Time shift 时间变换
Assume :
Then:
Time shift leads to unchanged amplitude and shifted phase.

## Slide 56: Fourier Series Properties
Time reversal 时间倒转
Assume :
Then:

## Slide 57: Fourier Series Properties
Time scaling 时间缩放
Assume :
Then:
Note that though Fourier series coefficients, , is unchanged, Fourier series representation is different, because each harmonic component is different: for , the harmonic frequency is for , it is .

## Slide 58: Fourier Series Properties
Multiplication 乘法
Assume :
Then:

## Slide 59: Fourier Series Properties
Conjugation 共轭
Assume :
Then:

## Slide 60: Fourier Series Properties
Conjugation
Even/Odd property
If is real ():

## Slide 61: Fourier Series Properties
Conjugation
Even/Odd property 偶/奇 属性
If is real and even ():
is real and even

## Slide 62: Fourier Series Properties
Conjugation
Even/Odd property
If is real and odd ():
is imaginary and odd虚构的,奇数的

## Slide 63: Fourier Series Properties
Parseval’s relation
The average power of a function in a period is equal to the sum of the square (power) of its Fourier series coefficients.
一个周期内函数的平均幂等于其傅立叶级数系数的平方和。

## Slide 64: Fourier Series Properties
Parseval’s relation帕塞瓦尔的关系
Proof:

## Slide 65
Thank you for your listening!