## Slide 1
Lecture 4 Fourier Series of Continuous-time Signals
School of Computer Engineering and Science
Shanghai University
Instructor: Shengyu Duan, Weiwei Chen

## Slide 2: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 3: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 4: Time/Frequency Domain
Time domain signal
A signal is a function, in the mathematical sense, normally a function of time.

## Slide 5: Time/Frequency Domain
Time domain signal
Time domain analysis examines the amplitude vs. time characteristics of a measuring signal.
Time domain is how people tend to think that things work, but in many situations, signals in time domain can be complicated.

## Slide 6: Time/Frequency Domain
Time domain signal
We can easily observe the loudness of a sound, but what else?
  - Whose voice is this?
  - How much is the noise?
An audio signal in time domain

## Slide 7: Time/Frequency Domain
Frequency domain
In 1807, J.B.J Fourier proposed to use trigonometric functions and series to solve heat equation in a metal plate.
Fourier claimed any arbitrary periodic function can be represented by a harmonically related trigonometric series.
Fourier series representation:

## Slide 8: Time/Frequency Domain

## Slide 9: Time/Frequency Domain

## Slide 10: Time/Frequency Domain
Frequency domain
Frequency domain shows how much of the signal lies within each given frequency band over a range of frequencies.
Time domain signal
Frequency domain signal

## Slide 11: Time/Frequency Domain
Why frequency domain is important
We can collect even more information in frequency domain, e.g.:
  - Speaker recognition based on frequency-based coefficients
  - Noise identification based on noise frequency characteristics
An audio signal in frequency domain

## Slide 12: Time/Frequency Domain
Why frequency domain is important
Frequency domain is a different perspective on signal, which providing us more useful information.
Generally,
- Time domain shows how we tend to think that things work;
  - Frequency domain can often provide many detailed performance specifications.

## Slide 13: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 14: Response of LTI Systems to Exponential Signal
Fourier series sine-cosine form
Sinusoids can be represented by complex exponential function

## Slide 15: Response of LTI Systems to Exponential Signal
Fourier series exponential form

## Slide 16: Response of LTI Systems to Exponential Signal
Fourier series exponential form
Assume

## Slide 17: Response of LTI Systems to Exponential Signal
Fourier series exponential form

## Slide 18: Response of LTI Systems to Exponential Signal
Assume
LTI

## Slide 19: Response of LTI Systems to Exponential Signal
LTI

## Slide 20: Response of LTI Systems to Exponential Signal
is a constant, thus we define :
LTI

## Slide 21: Response of LTI Systems to Exponential Signal
Response of a LTI system to an exponential signal is this exponential signal multiplied with a constant.
We call an exponential function, , as the eigenfunction of any LTI system.
We call the constant, , as the eigenvalue associated with the eigenfunction .

## Slide 22: Response of LTI Systems to Exponential Signal
Why do we specifically study LTI response to exponential signal?
Fourier series can be considered as a composition of exponential signals:

## Slide 23: Response of LTI Systems to Exponential Signal
Why do we specifically study LTI response to exponential signal?
LTI response to a periodic signal represented by Fourier series is still a periodic signal represented by Fourier series.
LTI

## Slide 24: Response of LTI Systems to Exponential Signal
If the input has a frequency component, the output will exactly have the same frequency component, except scaled by a constant.
Frequency domain:

## Slide 25: Response of LTI Systems to Exponential Signal
Each frequency component never split to other frequency components, no convolution involved, realizing fast and convenient signal processing.

## Slide 26: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 27: Fourier Series Representation
Harmonically related complex exponentials
A harmonic of such a wave is a wave with a frequency that is a positive integer multiple of the frequency of the original wave, known as the fundamental frequency.
Fundamental frequency: ()
2nd harmonic: 2 ()
3rd harmonic: 3 () …

## Slide 28: Fourier Series Representation
Determination of Fourier series coefficient -

## Slide 29: Fourier Series Representation
Determination of Fourier series coefficient -

## Slide 30: Fourier Series Representation
Determination of Fourier series coefficient -
For k=n:
For kn:

## Slide 31: Fourier Series Representation
Determination of Fourier series coefficient -

## Slide 32: Fourier Series Representation
Fourier series representation （傅里叶级数表示）:
Fourier series coefficient（傅里叶级数系数）:

## Slide 33: Fourier Series Representation
Example:
Find Fourier series coefficients for the following periodic signal.

## Slide 34: Fourier Series Representation
Solutions:

## Slide 35: Fourier Series Representation
Assume
Spectral:

## Slide 36: Fourier Series Representation
Assume
But is this correct?

## Slide 37: Fourier Series Representation
Fourier series sine-cosine form
Fourier series amplitude-phase form

## Slide 38: Fourier Series Representation
Amplitude-phase form derived from exponential form

## Slide 39: Fourier Series Representation
Amplitude-phase form derived from exponential form
Remember in slide 16, we have assumed: , thus and (for ) are a pair of complex conjugates.
and (for ) are a pair of complex conjugates.
and (for ) are also a pair of complex conjugates.

## Slide 40: Fourier Series Representation
Amplitude-phase form derived from exponential form
Remember in slide 16, we have assumed: , thus and (for ) are a pair of complex conjugates.
Note that the above hypothesis is true, only if and are real, and thus the signal is a real signal.

## Slide 41: Fourier Series Representation
Amplitude-phase form derived from exponential form
Remember in slide 16, we have assumed: , thus and (for ) are a pair of complex conjugates.
and (for ) are a pair of complex conjugates.
and (for ) are also a pair of complex conjugates.

## Slide 42: Fourier Series Representation
Amplitude-phase form derived from exponential form

## Slide 43: Fourier Series Representation
Amplitude-phase form derived from exponential form
Use polar coordinate system to represent as:

## Slide 44: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 45: Convergence Issue
Question:
In time domain, this signal is not continuous with discontinuity.
In frequency domain, this signal is represented by a trigonometric series, each of which is continuous.
How is the discontinuity represented?

## Slide 46: Convergence Issue
Gibbs phenomenon（吉伯斯现象）

## Slide 47: Convergence Issue
Gibbs phenomenon
The partial sum of the Fourier series has large oscillations near the jump, which might cause a fixed overshoot above the function itself.
As the number of terms rises, the error of the approximation is reduced in width and energy.
At the jump discontinuities, the limit will converge to the average of the values of the function on either side of the jump. (Dirichlet Theorem 狄利赫里定理)

## Slide 48: Convergence Issue
A period signal can be represented by Fourier series, if it has finite energy:

## Slide 49: Convergence Issue
Dirichlet’s condition（狄利赫里条件）
A signal can be represented by Fourier series expansion, if
(1) it is absolutely integrable,
(2) it has finite number of maxima & minima in a period
(3) it has finite number of discontinuities in a period

## Slide 50: Convergence Issue
Dirichlet’s condition
A signal can be represented by Fourier series expansion, if
(1) it is absolutely integrable,
The signal below can not be represented by Fourier series expansion:

## Slide 51: Convergence Issue
Dirichlet’s condition
A signal can be represented by Fourier series expansion, if
(2) it has finite number of maxima & minima in a period
The signal below can not be represented by Fourier series expansion:

## Slide 52: Convergence Issue
Dirichlet’s condition
A signal can be represented by Fourier series expansion, if
(3) it has finite number of discontinuities in a period
The signal below can not be represented by Fourier series expansion:

## Slide 53: Outline: Lecture 4: Fourier Series of Continuous-time Signals
Time/Frequency Domain
Response of LTI Systems to Exponential Signal
Fourier Series
Fourier Series Representation
Convergence Issue
Fourier Series Properties

## Slide 54: Fourier Series Properties
The following notation is used to indicate a signal, , can be represented by Fourier series with the coefficients, .

## Slide 55: Fourier Series Properties
Linearity
Assume :
,
Then:

## Slide 56: Fourier Series Properties
Time shift
Assume :
Then:
Time shift leads to unchanged amplitude and shifted phase.

## Slide 57: Fourier Series Properties
Time reversal
Assume :
Then:

## Slide 58: Fourier Series Properties
Time scaling
Assume :
Then:
Note that though Fourier series coefficients, , is unchanged, Fourier series representation is different, because each harmonic component is different: for , the harmonic frequency is for , it is .

## Slide 59: Fourier Series Properties
Multiplication
Assume :
Then:
Let

## Slide 60: Time/Frequency Domain

## Slide 61: 不同傅里叶级数表示形式的相互转换
解：首先回忆傅里叶级数表示的三种形式：
正余弦形式：
复指数形式：
幅度-相位形式：

## Slide 62: Fourier Series Properties
Conjugation
Assume :
Then:

## Slide 63: Fourier Series Properties
Conjugation
Even/Odd property
If is real ():

## Slide 64: Fourier Series Properties
Conjugation
Even/Odd property
If is real and even ():
is real and even

## Slide 65: Fourier Series Properties
Conjugation
Even/Odd property
If is real and odd ():
is imaginary and odd

## Slide 66: Fourier Series Properties
Parseval’s relation（帕斯瓦尔关系）
The average power of a function in a period is equal to the sum of the square (power) of its Fourier series coefficients.

## Slide 67: Fourier Series Properties
Parseval’s relation
Proof:

## Slide 68
Thank you for your listening!