## Slide 1
Lecture 7 Fourier Series of Discrete-time Signals
School of Computer Engineering and Science
Shanghai University
Instructor: Shengyu Duan, Weiwei Chen

## Slide 2: Outline: Lecture 7: Fourier Series of Discrete-time Signals
Discrete Time Fourier Series
Fourier Series Representation
Determination of Fourier Series Coefficient
Fourier Series Properties
Application Example
System Characterization
Filtering

## Slide 3: Outline: Lecture 7: Fourier Series of Discrete-time Signals
Discrete Time Fourier Series
Fourier Series Representation
Determination of Fourier Series Coefficient
Fourier Series Properties
Application Example
System Characterization
Filtering

## Slide 4: Discrete Time Fourier Series Representation
Discrete-time signal
A discrete-time signal is a time series consisting of a sequence of quantities, denoted by , where n is an integer value that varies discretely.
x[n]
n

## Slide 5: Discrete Time Fourier Series Representation
Periodic discrete-time signal
A discrete-time periodic signal satisfies , where N is the period. Thus, the frequency

## Slide 6: Discrete Time Fourier Series Representation
Fourier series
Any arbitrary periodic function can be represented by a harmonically related trigonometric series.
For continuous-time signal:
This should also be correct for discrete-time signal.

## Slide 7: Discrete Time Fourier Series Representation
Fourier series
For continuous-time signal:
For discrete-time signal:
Is k still located in the range of []?

## Slide 8: Discrete Time Fourier Series Representation
  Important Differences Between Continuous-time and Discrete-time Exponential/Sinusoidal Signals
      For discrete-time, signals with frequencies ω0 and
      ω0 +m．2π are identical. This is Not true for
      continuous-time.
Discrete-time:
Continuous-time:
重要！

## Slide 9: Continuous/Discrete Sinusoidals
Discrete-time:
(as m.n is an integer)
Continuous-time:
重要！

## Slide 10: Discrete Time Fourier Series Representation
2
3
5
4
0
1

## Slide 11: Discrete Time Fourier Series Representation
Fourier series
For discrete-time signal, consider the frequency for k+N:

## Slide 12: Discrete Time Fourier Series Representation
Fourier series
There are only N distinct frequencies for discrete-time signal. Those are:
or
or
……

## Slide 13: Discrete Time Fourier Series Representation
Discrete-time Fourier series representation
indicates N consecutive integers, e.g., [0, N-1], [1, N], [2, N+1], etc.

## Slide 14: Outline: Lecture 7: Fourier Series of Discrete-time Signals
Discrete Time Fourier Series
Fourier Series Representation
Determination of Fourier Series Coefficient
Fourier Series Properties
Application Example
System Characterization
Filtering

## Slide 15: Determination of Fourier Series Coefficient
Continuous-time Fourier series coefficient:
Discrete-time Fourier series coefficient:

## Slide 16: Determination of Fourier Series Coefficient
Determination of discrete-time Fourier series coefficient
Proof:

## Slide 17: Determination of Fourier Series Coefficient
Determination of discrete-time Fourier series coefficient
Proof:
For k=r:
For k:

## Slide 18: Determination of Fourier Series Coefficient
Determination of discrete-time Fourier series coefficient
Proof:

## Slide 19: Determination of Fourier Series Coefficient
Discrete-time Fourier series representation:
Discrete-time Fourier series coefficient:
There is no convergence issue for discrete-time Fourier series!

## Slide 20: Determination of Fourier Series Coefficient
Example
Find for the following discrete-time periodic signal

## Slide 21: Determination of Fourier Series Coefficient
Solution

## Slide 22: Determination of Fourier Series Coefficient
Solution

## Slide 23: Determination of Fourier Series Coefficient
Solution
For :

## Slide 24: Determination of Fourier Series Coefficient
Assume :

## Slide 25: Determination of Fourier Series Coefficient
Compute the partial sum for as follows:

## Slide 26: Outline: Lecture 7: Fourier Series of Discrete-time Signals
Discrete Time Fourier Series
Fourier Series Representation
Determination of Fourier Series Coefficient
Fourier Series Properties
Application Example
System Characterization
Filtering

## Slide 27: Fourier Series Properties
The following notation is used to indicate a signal, , can be represented by Fourier series with the coefficients, .

## Slide 28: Fourier Series Properties
Time scaling
Assume :
Then:
The period for is

## Slide 29: Fourier Series Properties
Multiplication
Assume :
Then:

## Slide 30: Fourier Series Properties
First difference
Based on time shift property:
Based on linearity property:

## Slide 31: Fourier Series Properties
Parseval’s relation
The average power of a function in a period is equal to the sum of the square (power) of its Fourier series coefficients.

## Slide 32: Outline: Lecture 8: Fourier Series of Discrete-time Signals
Discrete Time Fourier Series
Fourier Series Representation
Determination of Fourier Series Coefficient
Fourier Series Properties
Application Example
System Characterization
Filtering

## Slide 33: System Characterization
Assume
LTI

## Slide 34: System Characterization
For discrete-time signal and LTI system h:

## Slide 35: System Characterization
For arbitrary periodic signal
LTI

## Slide 36: System Characterization
and are frequency-related functions, known as frequency response.
If the input has a frequency component, the output will exactly have the same frequency component, except scaled by a constant.
Frequency domain:

## Slide 37: Outline: Lecture 7: Fourier Series of Discrete-time Signals
Discrete Time Fourier Series
Fourier Series Representation
Determination of Fourier Series Coefficient
Fourier Series Properties
Application Example
System Characterization
Filtering

## Slide 38: Filtering
Modifying the amplitude/phase of the different frequency components in a signal, including eliminating some frequency components entirely.
frequency-shaping filter （频率成形滤波器）
frequency-selective filter （频率选择滤波器）

## Slide 39: Filtering
Example: frequency-shaping filter
Amplify high frequency components
Amplitude:

## Slide 40: Filtering
Example: frequency-shaping filter
Amplitude:
Compress high frequency components

## Slide 41: Filtering
Example: frequency-selective filter
Ideal low-pass filter

## Slide 42: Filtering
Example: frequency-selective filter
Ideal low-pass filter
LTI
π

## Slide 43: Filtering
Example: frequency-selective filter
Ideal low-pass filter
LTI

## Slide 44: Filtering
Example: frequency-selective filter
Ideal low-pass filter
LTI

## Slide 45: Filtering
Example: frequency-selective filter
Ideal low-pass filter
LTI
0

## Slide 46: Filtering
Example: frequency-selective filter
Ideal filters (continuous-time signal)
(a)
(b)
(c)
Low-pass filter
High-pass filter
Band-pass filter

## Slide 47: Filtering
Example: frequency-selective filter
Ideal filters (discrete-time signal)
(a)
(b)
(c)
Low-pass filter
High-pass filter
Band-pass filter

## Slide 48
Thank you for your listening!